## Slide 1: Chapter 7: Enhanced Interior Gateway Protocol (EIGRP)
Scaling Networks
Notes: Cisco Networking Academy program
Scaling Networks
Chapter 7: Enhanced Interior Gateway Protocol (EIGRP)

## Slide 2: Chapter 7
7.0 Introduction
7.1 Characteristics of EIGRP
7.2 Configuring EIGRP for IPv4
7.3 Operation of EIGRP
7.4 Configuration of EIGRP for IPv6
7.5 Summary
Notes: Chapter 7

## Slide 3: Chapter 7: Objectives
Describe the features and operation of EIGRP.
Examine the different EIGRP packet formats.
Calculate the composite metric used by the Diffusing Update Algorithm (DUAL).
Describe the concepts and operation of DUAL.
Examine the commands to configure and verify basic EIGRP operations for IPv4 and IPv6.
Notes: Chapter 7 Objectives

## Slide 4: 7.1 Characteristics of EIGRP
Notes: Cisco Networking Academy program
Scaling Networks
Chapter 7: Enhanced Interior Gateway Protocol (EIGRP)

## Slide 5: Basic Features of EIGRP Features of EIGRP
Released in 1992 as a Cisco proprietary protocol.
2013 basic functionality of EIGRP released as an open standard.
Advanced Distance Vector routing protocol.
Uses the Diffusing Update Algorithm (DUAL) to calculate paths and back-up paths.
Establishes Neighbor Adjacencies.
Uses the Reliable Transport Protocol to provide delivery of EIGRP packets to neighbors.
Partial and Bounded Updates. Send updates only when there is a change and only to the routers that need the information.
Supports Equal and Unequal Cost Load Balancing.
Notes: 7.1.1.1 Features of EIGRP

## Slide 6: Basic Features of EIGRP Protocol Dependent Modules
Notes: 7.1.1.2 Features of EIGRP

## Slide 7: Basic Features of EIGRP Reliable Transport Protocol
Notes: 7.1.1.3 Reliable Transport Protocol

## Slide 8: Basic Features of EIGRP Authentication
EIGRP can be configured to authenticate routing information.
Ensures routers only accept updates from routers that have been configured with the correct authentication information.
Notes: 7.1.1.4 Authentication

## Slide 9: Types of EIGRP Packets EIGRP Packet Types
Notes: 7.1.2.1 EIGRP Packet Types

## Slide 10: Types of EIGRP Packets EIGRP Hello Packets
Used to discover EIGRP neighbors.
Used to form and maintain EIGRP neighbor adjacencies.
Sent as IPv4 or IPv6 multicasts.
IPv4 multicast address 224.0.0.10.
IPv6 multicast address FF02::A.
Unreliable delivery.
Sent every 5 seconds (every 60 seconds on low-speed NBMA networks).
EIGRP uses a default Hold timer of three times the Hello interval before declaring neighbor unreachable.
Notes: 7.1.2.2 EIGRP Hello Packets

## Slide 11: Types of EIGRP Packets EIGRP Update & Acknowledgement Packets
Update packets are sent to propagate routing information, only when necessary.
Sends Partial updates – only contains information about route changes.
Sends Bounded updates-sent only to routers affected by the change.
Updates use reliable delivery, therefore, require an acknowledgement.
Notes: 7.1.2.3 EIGRP Update & Acknowledgement Packets

## Slide 12: Types of EIGRP Packets EIGRP Query and Reply Packets
Used when searching for networks.
Queries use reliable delivery, which can be multicast or unicast.
Replies use reliable delivery.
Notes: 7.1.2.4 EIGRP Query and Reply Packets

## Slide 13: EIGRP Messages Encapsulating EIGRP Messages
Notes: 7.1.3.1 Encapsulating EIGRP Messages

## Slide 14: EIGRP Messages EIGRP Packet Header and TLV
Notes: 7.1.3.2 EIGRP Packet Header and TLV

## Slide 15: 7.2 Configuring EIGRP for IPv4
Notes: Cisco Networking Academy program
Scaling Networks
Chapter 7: Enhanced Interior Gateway Protocol (EIGRP)

## Slide 16: Configuring EIGRP with IPv4 EIGRP Network Topology
This course uses the topology that configures EIGRP with IPv4.
Notes: 7.2.1.1 EIGRP Network Topology

## Slide 17: Configuring EIGRP with IPv4 Autonomous System Numbers
The router eigrp autonomous-system command enables the EIGRP process.
The autonomous system number is only significant to the EIGRP routing domain.
The EIGRP autonomous system number is not associated with the Internet Assigned Numbers Authority (IANA) globally assigned autonomous system numbers used by external routing protocols.
Internet Service Providers (ISPs) require an autonomous system number from IANA.
ISPs often use the Border Gateway Protocol (BGP), which does use the IANA autonomous system number in its configuration.
Notes: 7.2.1.2 Autonomous System Numbers

## Slide 18: Configuring EIGRP with IPv4 Router EIGRP Command
Router(config)# router eigrp autonomous-system
To completely remove the EIGRP routing process from a device, use the no router eigrp autonomous-system command.
Notes: 7.2.1.3 The Router EIGRP Command

## Slide 19: Configuring EIGRP with IPv4 EIGRP Router ID
Used in both EIGRP and OSPF routing protocols, the router ID’s role is more significant in OSPF.
Notes: 7.2.1.4 EIGRP Router ID

## Slide 20: Configuring EIGRP with IPv4 Configuring the EIGRP Router ID
Configuring the EIGRP router ID
Router(config)# router eigrp autonomous-system
Router(config-router)# eigrp router-id ipv4-address
The IPv4 loopback address can be used as the router ID.
If the eigrp router-id value is not configured, the highest loopback address is selected as the router ID.
Configuring a loopback interface
Router(config)# interface loopback number
Router(config-if)# ip addressipv4-address subnet-mask
Notes: 7.2.1.5 Configuring the EIGRP Router ID

## Slide 21: Configuring EIGRP with IPv4 Network Command
Enables any interface on this router that matches the network address in the network router configuration mode command to send and receive EIGRP updates.
These networks are included in EIGRP routing updates.
Notes: 7.2.1.6 The Network Command

## Slide 22: Configuring EIGRP with IPv4 Network Command
The eigrp log-neighbor-changes router configuration mode
  On by default
  Displays changes in neighbor adjacencies
  Verifies neighbor adjacencies during configuration
  Indicates when any adjacencies have been removed
Notes: 7.2.1.6 The Network Command

## Slide 23: Configuring EIGRP with IPv4 The Network Command and Wildcard Mask
To configure EIGRP to advertise specific subnets only, use the wildcard-mask option with the network command.
Router(config-router)# network network address [wildcard-mask]
The wildcard mask is the inverse of the subnet mask.
To calculate the wildcard mask, subtract the subnet mask from 255.255.255.255:
  255.255.255.255
  -- 255.255.255.252
0. 0. 0. 3 wildcard mask
Note: Some IOS versions also let you enter the subnet mask instead of a wildcard mask.
Notes: 7.2.1.7 The Network Command and Wildcard Mask

## Slide 24: Configuring EIGRP with IPv4 Passive Interface
Use the passive-interface command to:
    Prevent neighbor adjacencies
    Suppress unnecessary update traffic
    Increase security controls, such as preventing unknown rogue routing devices from receiving EIGRP updates
To configure:
  Router(config)# router eigrp as-number
  Router(config-router)# passive-interface interface-type interface-number
To verify:
  Router# show ip protocols
Notes: 7.2.1.8 Passive Interface

## Slide 25: Configuring EIGRP with IPv4 Verifying EIGRP: Examining Neighbors
Notes: 7.2.2.1 Verifying EIGRP: Examining Neighbors

## Slide 26: Configuring EIGRP with IPv4 Verifying EIGRP: show ip protocols Command
Notes: 7.2.2.2 Verifying EIGRP: Show ip protocols command

## Slide 27: Configuring EIGRP with IPv4 Verifying EIGRP: Examine the IPv4 Routing Table
Notes: 7.2.2.3 Verifying EIGRP: Examine the IPv4 routing table

## Slide 28: 7.3 Operation of EIGRP
Notes: Cisco Networking Academy program
Scaling Networks
Chapter 7: Enhanced Interior Gateway Protocol (EIGRP)

## Slide 29: EIGRP Initial Route Discovery EIGRP Neighbor Adjacency
Notes: 7.3.1.1 EIGRP Neighbor Adjacency

## Slide 30: EIGRP Initial Route Discovery EIGRP Topology Table
Notes: 7.3.1.2 EIGRP Topology Table

## Slide 31: EIGRP Initial Route Discovery EIGRP Convergence
Convergence – All routers have the correct, most up-to-date information about the network.
Notes: 7.3.1.3 EIGRP Convergence

## Slide 32: Metrics EIGRP Composite Metric
Notes: 7.3.2.1 EIGRP Composite Metric

## Slide 33: Metrics Examining Interface Values
BW – Bandwidth of the interface (in Kilobits per second).
DLY – Delay of the interface (microseconds).
Reliability – Reliability of interface; by default, the value is not included in the computing metric.
Txload, Rxload – By default, the value is not included in the computing metric.
Notes: 7.3.2.2 Examining Interface Values

## Slide 34: Metrics Bandwidth Metric
Use the show interfaces command to verify bandwidth.
Most serial bandwidths are set to 1,544 kb/s (default).
A correct value for bandwidth is very important in order to calculate the correct metric (both sides of link must have same bandwidth).
Notes: 7.3.2.3 Bandwidth Metric

## Slide 35: Metrics Delay Metric
Notes: 7.3.2.4 Delay Metric

## Slide 36: Metrics Calculating the EIGRP Metric
Step 1. Determine the link with the slowest bandwidth. Use that value to calculate bandwidth (10,000,000/bandwidth).
Step 2. Determine the delay value for each outgoing interface on the way to the destination. Add the delay values and divide by 10 (sum of delay/10).
Step 3. Add the computed values for bandwidth and delay, and multiply the sum by 256 to obtain the EIGRP metric.
Notes: 7.3.2.5 Calculating the EIGRP Metric

## Slide 37: DUAL and the Topology Table DUAL Concepts
  Diffusing Update ALgorithm (DUAL) provides the following:
    Loop-free paths and loop-free backup paths
    Fast convergence
    Minimum bandwidth usage with bounded updates
  The decision process for all route computations is done by the DUAL Finite State Machine (FSM)
    DUAL FSM tracks all routes.
    Uses EIGRP metrics to select efficient, loop-free paths.
    Identifies the routes with the least-cost path to be inserted into the routing table.
  EIGRP maintains a list of backup routes that DUAL has already determined that can be used immediately if the primary path fails.
Notes: 7.3.3.2 Introduction to DUAL

## Slide 38: DUAL and the Topology Table Successor and Feasible Distance
  The Successor is the least-cost route to the destination network.
  The Feasible Distance (FD) is the lowest calculated metric to reach the destination network.
Notes: 7.3.3.3 Successor and Feasible Distance

## Slide 39: Feasible Successors, Feasibility Condition, and Reported Distance
  Feasible Successor (FS) is a neighbor that has a loop-free backup path to the same network as the successor, and it satisfies the Feasibility Condition (FC).
  Feasibility Condition (FC) is met when a neighbor’s Reported Distance (RD) to a network is less than the local router’s feasible distance to the same destination network.
  Reported Distance (RD) is an EIGRP neighbor’s feasible distance to the same destination network.
Notes: 7.3.3.4 Feasible Successors, Feasibility Condition and Reported Distance

## Slide 40: DUAL and the Topology Table Topology Table: show ip eigrp Command
Notes: 7.3.3.5-6 Topology Table: Show ip eigrp Command

## Slide 41: DUAL and the Topology Table Topology Table: No Feasible Successor
Notes: 7.3.3.7 Topology Table: No Feasible Successor

## Slide 42: DUAL and Convergence DUAL Finite State Machine (FSM)
Notes: 7.3.4.1 DUAL Finite State Machine (FSM)

## Slide 43: DUAL and Convergence DUAL: Feasible Successor
Notes: 7.3.4.2 DUAL: Feasible Successor

## Slide 44: DUAL and Convergence DUAL: No Feasible Successor
Notes: 7.3.4.3 DUAL: No Feasible Successor

## Slide 45: 7.4 Configuration of EIGRP for IPv6
Notes: Cisco Networking Academy program
Scaling Networks
Chapter 7: Enhanced Interior Gateway Protocol (EIGRP)

## Slide 46: EIGRP for IPv4 vs. IPv6 EIGRP for IPv6
Notes: 7.4.1.1 EIGRP for IPv6

## Slide 47: EIGRP for IPv4 vs. IPv6 Comparing EIGRP for IPv4 and IPv6
Notes: 7.4.1.2 Comparing EIGRP for IPv4 and IPv6

## Slide 48: EIGRP for IPv4 vs. IPv6 IPv6 Link-local Addresses
Notes: 7.4.1.3 IPv6 Link-local Addresses

## Slide 49: Configuring EIGRP for IPv6 EIGRP for IPv6 Network Topology
Notes: 7.4.2.1 EIGRP for IPv6 Network Topology

## Slide 50: Configuring EIGRP for IPv6 Configuring IPv6 Link-Local Addresses
  Manually configuring link-local addresses
  Verifying link-local addresses
Notes: 7.4.2.2 Configuring IPv6 Link-local Addresses

## Slide 51: Configuring EIGRP for IPv6 Configuring EIGRP for the IPv6 Routing Process
  The ipv6 unicast-routing global configuration mode command is required to enable any IPv6 routing protocol.
  Configuring EIGRP for IPv6
  The no shutdown command and a router ID are required for the router to form neighbor adjacencies.
Notes: 7.4.2.3 Configuring EIGRP for IPv6 Routing Process

## Slide 52: Configuring EIGRP for IPv6 ipv6 eigrp interface Command
  Enabling EIGRP of IPv6 on an Interface
Notes: 7.4.2.4 ipv6 eigrp Interface Command

## Slide 53: Verifying EIGRP for IPv6 Verifying EIGRP for IPv6: Examining Neighbors
Notes: 7.4.3.1 Verifying EIGRP for IPv6:Examining Neighbors

## Slide 54: Verifying EIGRP for IPv6 Verifying EIGRP for IPv6: show ip protocols Command
Notes: 7.4.3.2 Verifying EIGRP for IPv6: show ip protocols command

## Slide 55: Verifying EIGRP for IPv6 Verifying EIGRP for IPv6: Examine the Routing Table
  Use the show ipv6 route command to examine the IPv6 routing table.
Notes: 7.4.3.3 Verifying EIGRP for IPv6: Examine the Routing Table

## Slide 56: Chapter 7: Summary
  EIGRP is a classless, advanced distance vector routing protocol.
  EIGRP uses the source code of “D” for DUAL in the routing table.
  The default administrative distance of 90 is used for internal routes and 170 for routes imported from an external source.
  Advanced features include DUAL, establishing neighbor adjacencies, RTP, partial and bounded updates, and equal and unequal cost load balancing.
  PDMs give EIGRP the capability to support different Layer 3 protocols.
  EIGRP Hello packets are used to discover neighbors.
  The show ip eigrp neighbors command is used to view neighbor table and verify adjacencies.
Notes: 7.5 Summary

## Slide 57: Chapter 7: Summary (cont.)
  EIGRP sends partial bounded updates when a change occurs on network.
  EIGRP composite metric uses bandwidth, delay, reliability and load to determine the best path (by default, only bandwidth and delay are used).
  DUAL FSM is used to determine best path; Successor and potential backup path, FS to every destination network.
Notes: 7.5 Summary (cont.)